## Slide 1
CHAPTER 3: TRANSISTOR MOSFET
Trang Ho
VKU, Jan-2024
1

## Slide 2: Chapter 3: MOSFET
Introduction
Classifications
  JFET
  D-FET (Depletion MOS)
  MOSFET (Enhancement E-FET)
DC biasing
Small signal analysis
Equivalent small signal circuit

## Slide 3: FET Introduction
High input impedance, nMΩ-n100MΩ
Controlled by voltage (≠ BJT)
Low power consumption
Low noise, suitable for small signal
Low impact of temperature
Using as switch for low power application
Small size and adapt for integrated circuit

## Slide 4: Classification
JFET-Junction Field Effect Transistor
🞑 N and P channels
MOSFET-Metal Oxide Semiconductor FET
🞑 Depletion MOS
  N and P channels
🞑 Enhancement MOS
  N and P channels

## Slide 5: Classification (cont’d)
 JFET  D-FET
E-FET (MOSFET)

## Slide 6: JFET
Structure and Operation
Characteristic Curve
Compare with BJT
Examples, datasheets

## Slide 7: JFET – Structure
7

## Slide 8: JFET – Operation
VGS = 0, VDS>0 increase gradually, ID increases and then saturates

## Slide 9: JFET – Operation
VGS = 0, VDS = VP, ID = IDSS
VP : pinch off voltage (pinch-off)
ID = IDSS(1 - VGS/VP)2

## Slide 10: JFET – Operation
VGS < 0, VDS > 0, Saturation current reduces when VGS  Vpinch-off
VGS = VP, ID = 0

## Slide 11: JFET – Characteristic Curves
ID = f(VGS) Shockley equation:
IG ≈ 0A
ID = IS
(gate current)
(ID drain current, IS source current)
ID = IDSS(1 - VGS/VP)2

## Slide 12: JFET – Characteristic Curves
P-channel, IDSS = 6mA, VP = 6V
N-channel, IDSS = 8mA, VP = - 4V

## Slide 13: JFET – Symbol
13

## Slide 14: JFET
2N5457
14

## Slide 15: Datasheet-2N5457
Rating | Symbol | Value | Unit
Drain-Source voltage | VDS | 25 | Vdc
Drain-Gate voltage | VDG | 25 | Vdc
Reverse G-S voltage | VGSR | -25 | Vdc
Gate current | IG | 10 | nAdc
Device dissipation 250C Derate above 250C | PD | 310 2.82 | mW mW/0C
Junction temp range | TJ | 125 | 0C
Storage channel temp range | Tstg | -60 to +150 | 0C

## Slide 16: Datasheet-2N5457-characteristics
Characteristic | Symbol | Min | Typ | Max | Unit
VG-S breakdown | V(BR)GSS | -25 |  |  | Vdc
Igate reverse(Vgs=-15, Vds=0) | IGSS |  |  | -1.0 | nAdc
VG-S cutoff | VGS(off) | -0.5 |  | -1.0 | Vdc
VG-S | VGS |  | -2.5 | -6.0 | Vdc
ID-zero gate volage | IDSS | 1.0 | 3.0 | 5.0 | mAdc
Cin | Ciss |  | 4.5 | 7.0 | pF
Creverse transfer | Crss |  | 1.5 | 3.0 | pF

## Slide 17: MOSFET
Structures
Operation
Characteristic Curves

## Slide 18: MOSFET – Structure
N-channel Enhancement EMOS
N-channel Depletion DMOS

## Slide 19: MOSFET – Operation
N-channel EMOS
VGS > VTH, VDS > 0
N-channel DMOS
VGS = 0, VDS > 0

## Slide 20: DMOS – Transfer characteristic curves
Similar to JFET, transfer characteristic curve ID = f(VGS)
follows Shockley equation: ID = IDSS(1 - VGS/VP)2
Can work at: VGS > 0, ID > 0

## Slide 21: EMOS – Transfer characteristic curve
Transfer characteristic curve:
ID = k(VGS – VT)2 with VT > 0 (for NMOS) and Vt< 0 for PMOS)
When VGS < VT, ID = 0

## Slide 22: MOSFET – Transfer characteristic curve
P-channel depletion

## Slide 23: MOSFET – Transfer characteristic curve
P-channel enhancement

## Slide 24: MOSFET – Symbol
EMOS
DMOS

## Slide 25: EMOS 25 2N4351

## Slide 26: Datasheet-2N4351-EMOS
Characteristic | Symbol | Min | Max | Unit
VDS breakdown | V(BR)DSX | 25 |  | Vdc
ID-zero gate volage, Vds=10V,Vgs=0, 25C – 150C | IDSS |  | 10 10 | nAdc µAdc
Igate reverse(Vgs=+-15, Vds=0) | IGSS |  | +-10 | nAdc
VDS on Voltage | VDS(on) |  | 1.0 | V
Cin(Vds=10V,Id=2mA,f=140kHz) | Ciss |  | 5.0 | pF
CDS(Vdsub=10V,f=140KHz) | Crss |  | 5.0 | pF
RDS(Vgs=10V,Id=0,f=1KHz) | Rds(on) |  | 300 | ohms

## Slide 27: VMOS
VMOS – Vertical MOSFET, increase channel length
Increase drain current thanks to large space of heat release
High switching speed

## Slide 28: Resume
JFET
DFET
MOSFET

## Slide 29: CMOS
CMOS=Complementary MOSFET
pMOS và nMOS: fabricated on same wafer
Reduce size and power consumption, increase switching speed
Analog/Digital IC design

## Slide 30: Biasing types
Fixed bias
  Self-biasing
Voltage divider biasing
Feedback biasing

## Slide 31: Some noted
With all kinds of FET:
IG = 0A ID = IS
For JFET & D-MOSFET:
ID = IDSS(1 – VGS/VP)2
For E-MOSFET (MOSFET):
ID = k(VGS – VT)2 (saturation mode)
Determine Q-point (DC operating point) and DC load line

## Slide 32: Fix biasing (ex: JFET)
IG = 0A
VS = 0
VGS = VG = - VGG ID = IDSS(1-VGS/Vp)2
VG is fixed at VGG

## Slide 33: Fix biasing
ID = IDSS(1-VGS/VP)2
Build transfer characteristic curve from this table:
VGS | ID
0 | IDSS
0.3VP | IDSS/2
0.5Vp | IDSS/4
VP | 0mA
DC load line:
VGS = - VGG
Intersection between DC load
line and trans. Charact. Curve
 Q point

## Slide 34: Temperature effect
Leakage current IGSS increases when t0 increases  cannot neglect RG at mentioned previously so:
Q will move from :
VGS = VGG + IGSS*RG
new Q-point

## Slide 35: Impact of temperature
Question: If VGG=-1V& RG=1 MΩ. IGSS=1nA at 25°C and increase
double when temperature increases 10oC. Determine VGS at 125oC ?

## Slide 36: Impact of temperature
new Q-point
Answer:
At 25oC, IGSS×RG=10-9×106 = 1mV, can
be neglected when compare with VGG= -
1V (or new VGS= -999mV).
Q point at 1250C is shifted to a new point and it is far from the initial Q point at room temperature
Question: If VGG=-1V& RG=1 MΩ. IGSS=1nA at 25°C and increase double when temperature increases 10oC. Determine VGS at 125oC ?
When Temp. increases to 125oC, current IGSS increases to 210 times ( ≈103)
IGSS = 103 ×1nA =1µA
IGSS× RG=1µA* 1MOhm = 1V
New Q point: VGS = 0V & ID = IDSS

## Slide 37: Self biasing
What is the main difference compared to fixed biasing?
Role of RS?
Remove RG to reduce impact of temperature?

## Slide 38: Self-biasing
Loop at input:
IG = 0 => VG = 0V  VGS = - ISRS (1)
ID = IDSS(1-VGS/Vp)2 (2)
To determine Q point:
 Sole the equation system: (1) + (2)
 Or by using curve method as shown in the paragraph (intersection point)
Consider the impact of Temp.?

## Slide 39: Voltage divider biasing (ex: JFET)
IG = 0, output current ID is controlled by VGS
This biasing method is usually used for FET

## Slide 40: Voltage divider biasing (ex: JFET)
VG = VDDR2/(R1+R2)
 DC load line is: VGS = VG- IDRS (1)
RS varies  shift of Q point and DC load line
Characteristic curve of FET ID = IDSS(1-VGS/VP)2 , (2)
To determine Q point:
 Sole the equation system: (1)+(2)
 Or by using curve method as shown in the paragraph (intersection point)

## Slide 41: Voltage divider biasing (ex: DMOSFET)
VG = VDD* 10MΩ/(110MΩ+10MΩ)
 DC load line: VGS = VG – IS*750Ω (1)
ID current of DMOS:
ID = IDSS(1-VGS/VP)2 (2)
To determine Q point:
 Sole the equation system: (1) + (2)
 Or by using curve method as shown in the paragraph (intersection point)

## Slide 42: Voltage divider biasing (ex: DMOSFET)
With DMOS: ID = IDSS(1-VGS/VP)2
VGS can be positive

## Slide 43: Voltage divider biasing (E-MOSFET)
With EMOS:
ID = k(VGS-VT)2
k=IDon/(VGSon-VT)2

## Slide 44: Voltage divider biasing (ex: E-MOSFET)
With EMOS: ID = k(VGS-VT)2
where k = ID-on/(VGSon-VT)2
Draw transfer characteristic
curve of E-MOSFET

## Slide 45: Feedback biasing (ex: E-MOSFET)
At the node G:
IG = 0  VG = VD


## Slide 46: Feedback biasing (ex: E-MOSFET)
At the node G: IG = 0 => VG = VD
DC load line
(2)
VGS = VDS = VDD - RDID (1)
Transfer char. equation: ID = k(VGS - VT)2 ,
k = IDon/(VGSon-VT)2
Solve equ. Sys. (1,2) or use paragraph method

## Slide 47: Example
Question: Determine Q (ID, VGS) point Q of these circuits?

## Slide 48: Example
Question: Determine Q (ID, VGS) point Q of these circuits?

## Slide 49: Example
Question: Determine VGS and
VDS
for the E-MOSFET circuit
above. Given that this MOSFET has minimum values of ID(on) = 200 mA at VGS = 4V and Vth = 2V.
Question: Determine ID with Vth = 3V.

## Slide 50: Analyze the circuit for AC signal (small signal)
51

## Slide 51: Small signal model
52

## Slide 52: Transconductance
gm = ∆ID / ∆VGS = d(ID(VGS))
Derivation of current ID as function of VGS
Slope of ID(VGS) at Q point

## Slide 53: Transconductance gm (JFET & DMOS)

VP VP 
For E-MOS; gm is defined from Shockley equation:
gm  2IDSS 1  VGS 
When VGS = 0:
gm0  2IDSS
VP
gm determined at Q point:

P 
V 
gm gm0   VGS 
1

## Slide 54: Transconductance gm (E-MOSFET)
For JFET & DMOS, gm is defined from:
gm determined at Q point:

## Slide 55: AC equivalent circuit (EMOS)
Notes:
VGS should be positive for NMOS and negative for PMOS
gm = 2k(VGS – VT)

## Slide 56: 3 types of MOSFET amplifier
CS – CD – CG

## Slide 57: EMOS – CS with fixed bias voltage
Vout
Vin Cin
+ V1
10V
VDD
RG
RD
Cout N-EMOS
Input at G terminal, output at D
terminal  Common Source
Fixed biasing (S grounded)
To draw AC equivalent circuit
  Short circuit all capacitors
  Short circuit power supply
AC equivalent
circuit

## Slide 58: EMOS – CS with fixed bias voltage
Zi = RG
Zo = rd//RD
≈ RD
if rd > 10RD
AV = - gm(rD//RD) ≈ - gmRD if rd > 10RD
Input and output voltage are out of phase

## Slide 59: EMOS – CS with voltage divider
Input at G terminal, output at D terminal  Common Source
Voltage divider
S terminal is connected to Rs and Cs in parralel
G
D
S
R1
Cs
RS
Cout
Vout
C1
Vin 1uF
VDD
R2
RD
N-EMOS
AC equivalent circuit

## Slide 60: EMOS – CS with voltage divider
Zi = R1// R2 |  | 
Zo = rd//RD | ≈ RD | nếu rd > 10RD
AV = -gm(rD//RD) | ≈ gmRD | nếu rd > 10RD
Input and output voltage are out of phase

## Slide 61
EMOS – CS with voltage divider and wo. Cs
Input at G terminal, output at D terminal  Common Source
Voltage divider
S terminal is connected to ONLY Rs and REMOVE bypass-capacitor CS
G
D
S
R1
Cout
Vout
C1
Vin 1uF
VDD
R2
RD
N-EMOS
RS XCs
AC equivalent circuit
?????

## Slide 62: EMOS – CS with voltage divider and wo. Cs
Input at G terminal, output at D terminal  Common Source
Voltage divider
S terminal is connected to ONLY Rs and REMOVE bypass-capacitor CS
G
D
S
R1
Cout
Vout
C1
Vin 1uF
VDD
R2
RD
N-EMOS
RS XCs
AC equivalent circuit

## Slide 63: EMOS – CS with voltage divider and wo. Cs
Zi = RG (or R1//R2) Zo = RD/[1+gmRS+(RD+RS)/rd]
AV = -gmRD/[1+gmRS+(RD+RS)/rd]
Input and output voltage are out of phase

## Slide 64: EMOS – CS with feedback bias
Input at G terminal, output at D terminal: Common Source
Feedback biasing
To draw AC equivalent circuit
  Short circuit all capacitors
  Short circuit power supply

## Slide 65: EMOS – CS with feedback bias
AC equivalent circuit
  Short circuit all capacitors
  Short circuit power supply


## Slide 66: EMOS – CS with feedback bias
Zi = (RF+rd//RD)/[1+gm(rd//RD)]
≈ RF/(1+gmRD) with rd >10RD, RF>>rd//RD
Zo = RF//rd//RD ≈ RD with rd >10RD, RF>>rd//RD
AV = gm RF//rd//RD ≈ gmRD with rd >10RD, RF>>rd//RD
Output and input voltage are out of phase

## Slide 67: EMOS – CS with feedback bias
68

## Slide 68: EMOS – CS with feedback bias
69

## Slide 69: EMOS – CS with feedback bias
70

## Slide 70: JFET – CD with fixed biasing
Input at G terminal, output at S terminal: Common Drain
Fixed biasing

## Slide 71: JFET – CD with fixed biasing
Zi = RG
Zo = rd//RS//(1/gm) ≈ RS//(1/gm)
if rd > 10RS
AV = -gm(rd//RS)/[1+gm(rd//RS)] ≈ gmRS/[1+gmRS)]
≈ 1
if rd > 10RS
if gmRS >> 1

## Slide 72: JFET – CG with fixed biasing
Input at S terminal, output at D terminal:
Common GATE
Fixed biasing

## Slide 73: JFET – CG with fixed biasing
Zi = Rs//[(rd+RD)/(1+gmrd)] | ≈ RS//(1/gm) | nếu rd >10RD
Zo = rd//RD | ≈ RD | nếu rd >10RD
AV = [gmRD+ (RD/rd)]/[1+ RD/rd] | ≈ gmRD | nếu rd >10RD
Input and output voltage are IN-PHASE

## Slide 74: Equivalent circuit for DMOS
Similar to JFET and E-MOSFET
For DMOS:
  VGS can be positive for Nchannel and negative for P channel
  gm can be higher than gm0

## Slide 75: Resume
77

## Slide 76: Resume
78